## Slide 1
click Options to bring up the dialogue box
ensure
Unroll Rotation Curves is checked

## Slide 2
Wand wave data being collected
After the wand wave the cameras will appear in a circular form (it is not until you Set Origin that they “look correct”)
status window where overall error indicator will appear
cameras not in a circle? Ignore number, start again
Calibration Steps
Auto Masking (clean)
Wand Wave (gather data)
Set Origin (cameras orient)
Calibrate Floor Plane (slight adjustment – good for feet)
Save Calibration

## Slide 3
Studio Activities Tab
connect the cameras
gearbox will go red when connected
circle fit - calibrate cameras, solve or reconstruct -capture
streaming
layout for camera calibration
layout for ROM capture/process
layout for capture

## Slide 4
Post Processing Tab
Reconstruct Auto Label Solve Motion
new feature steps processed frame per frame

## Slide 5
Editors Tab
useful when streaming
(Server Active/Stream Offline Data)
script writing (hsl)

## Slide 6
Studio Activities tab
Circle Fit
Camera Layout
be sure this is set to Automatic

## Slide 7
1. Reconstruct 2. Auto Label 3. Solve Motion
Post Processing tab

## Slide 8
Left Hand from Above (no fingers)
In the Selection Filter
check none and then
Marker
Use the
Marker Editing Editor
with a marker selected Find Gap or Swap Markers
LOHAND_LeftHand
LOWR_LeftForeArm
LIWR_LeftForeArm
LIHAND_LeftHand

## Slide 9
Left Hand from Above with fingers
LIWR_LeftForeArm
LTHM3
LOWR_LeftForeArm
LIHAND_LeftHand
LOHAND_LeftHand
LPNK3
LIDX3

## Slide 10
Back View
Front View

## Slide 11
After Swap
Markers are repaired along with labeling After Swap
Bones are aligned properly After Calibrate
TIP: use ALT to select
After Calibrate

## Slide 12
After Reconstruct
Hint: 3.5 – adjust marker size
After Create Labeling Setup
After Label ROM
After Calibrate
(grey areas indicate covariance errors)
Reconstruct
Create Labeling Setup
Label ROM
Calibrate
(remember to check settings)

## Slide 13
After Solving

## Slide 15
In reconstruction settings you can set Minimum Cameras to Start Trajectory to 2 (default is 2) and Store Ray Contributions to False.
In Axiom Labeling Settings
Joint Ranges Slack default is 1, DO NOT go over 1.5, but 1.2 might be for a very flexible actor. The lower value will be more accurate.
Booting quality leave as is – zero will be doing best for system
Under Solving Settings: Turn Extrapolate finger data on to True
This only applies if you are using the Post (Axiom) Processing